Image/Video capture with V4L2
Meetup Linux Embarqué Toulouse, 05/12/2018

---
Who am I
- Alexis Lothoré, embedded software engineer
  - 2016 to 2018 : Smile ECS, Toulouse
  - 2018 to now : Somfy Protect By Myfox, Toulouse
- Main work fields :
  - Complete linux firmwares for embedded systems
  - Connected alarm systems : video streaming, connected systems, embedded security
https://github.com/Tropicao

---
Summary
- What is V4L2
- Using V4L2 for video capture : initialization, stream loop
- Going further : encoding a raw image for image, for video

---
What is V4L2
- A standardized kernel ↔ userspace API, started from kernel 2.1.X for v1, then dropped and replaced by v2 in v2.5.x
- Originally supports various captures support (webcams, TV tuners, radio)
- Now supports a large set of features : input/output for audio/video, tuners, modulators, extended user controls, M2M, etc.
- This presentation focuses on video capture

---
Why should I use V4L2 ?
One code base to rull them all !
Can adapt to each platform at runtime (e.g. capabilities detection)
But : you need proper V4L2 support (kernel and drivers)

---
What do you need to begin
- Obviously, a video capture device
- A V4L2 capable linux-kernel
- Proper V4L2 driver for used device

---
Your new friend : the official V4L2 doc
Can be used as an API documentation
Can be used as a guide
Userspace API, but also kernel API
The rest of the slides are heavily relying on this documentation
https://linuxtv.org/downloads/v4l-dvb-apis/uapi/v4l/v4l2.html

---
Discovering your device
struct v4l2_capability cap ;
dev_fd = open("/dev/video0", O_RDWR, 0) ;
if(ioctl(dev_fd, VIDIOC_QUERYCAP, &cap) == -1)
fprintf(stderr, "Cannot fetch devices capabilities") ;
if (!(cap.capabilities & V4L2_CAP_VIDEO_CAPTURE))
fprintf(stderr, "Selected device cannot capture video") ;

---
Configuring your device input
- setting the application priority :	VIDIOC_S_PRIORITY
- querying / setting video input :	VIDIOC_ENUMINPUT, VIDIOC_S_INPUT
- querying / setting video standards :	VIDIOC_ENUMSTD
- cropping :	VIDIOC_S_SELECTION
- setting streaming parameters	 	VIDIOC_S_PARM
- and more...

---
User controls on image
- A driver can expose many image controls (brightness, saturation, …)
- We can enumerate and expose those controls : VIDIOC_QUERYCTRL, VIDIOC_QUERY_EXT_CTRL
- Some controls can be menus : VIDIOC_QUERYMENU
- /!\ VIDIOC_QUERY_EXT_CTRL added later, check if supported by your kernel/driver !

---
The pixel format : quick summary
- Many different image formats are available, depends on drivers :
  - different colorspaces : RGB, HSL, YCbCr…
  - single plane or multi plane format
  - indexed formats
  - etc
- Each format is represented with a FourCC code
RGB format
YCbCr format
HSL format

---
Image format example : Bayer RGB
- FourCC code : ‘B’ ‘A’ ‘8’ ’1’
- Raw frame size : width * height
- Why more G than B and R ? Because human eye is more sensible to green !
...
B
G
B
G
B
G
B
G
...
G
R
G
R
G
R
G
R

---
Image format example : YUV422, or YUY2
- FourCC code : ‘Y’ ‘U’ ‘Y’ ’V’
- Raw frame size : width * height * 2
- Why more Y than U and V ? Because most of the image information is in Luma !
...
Y
U
Y
V
Y
U
Y
V

---
Image format example : NV12, or YUV420SP
- FourCC code : ‘N’ ‘V’ ‘1’ ’2’
- Raw frame size : width * height * 3/2
Y
Y
Y
Y
U
V
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
U
V
U
V
U
V
Y
Y
Y
Y

---
Negotiating image format
- Asking driver format capabilities : VIDIOC_ENUM_FMT
- Each format as a unique code, represented with 4 letters : FourCC code
- Selecting a format : VIDIOC_S_FMT
  - fill the v4l2_format structure according to your needs
  - format is not expressed the same way between APIs (single vs multiplanar)
  - remember to check what the driver has really taken !

---
Choosing a capture method
- Three way of retrieving raw frames :
  - basic I/O : read/write directly from/to device (remember to check for device capabilities : V4L2_CAP_READWRITE !)
  - streaming (needs V4L2_CAP_STREAMING !) :
    - memory mapping : request, mmap, enqueue and dequeue buffers
    - user pointers
    - DMA buffers (to export data between devices)

---
Focusing on MMAP buffers
VIDIOC_REQBUFS
- Allocate buffers on driver side( set number of buffers, and type V4L2_MEMORY_MMAP
- For each buffer, query length and location
- mmap the buffer
VIDIOC_QUERYBUF
VIDIOC_QUERYBUF
VIDIOC_QUERYBUF
mmap()
mmap()
mmap()
=> How many buffers do I need ???

---
The capture loop
VIDIOC_QBUF
VIDIOC_STREAMON
want frames ?
VIDIOC_DQBUF
process_buffer
VIDIOC_STREAMOFF
VIDIOC_QBUF

---
Using raw images in real world ?
Displaying raw images
http://www.rawpixels.net/
Encoding images :
we can pass raw RGB or YUV images to a JPEG encoder (software encoder, like jpeglib, or even a hardware JPEG encoder)

---
Exploiting raw frames for video
frame.aac
frame.raw
frame.h264
vid.mp4
Userspace
x264
libmp4v2
Kernel
V4L2
driver

---
Exploiting raw frames for video
frame.aac
frame.raw
frame.h264
vid.mp4
Userspace
libmp4v2
V4L2
driver
Hardware
codec
Kernel

---
Summary
( )
- Let’s face it : it was quite fastidious, just to get images…
- And we have just reinvented part of the wheel : see v4l2-ctl, v4l2ucp
- see also : libv4lconvert, libv4l, libv4l2
- libcamera, made to replace V4L2 ?
[Speaker Notes: ffmpeg -f video4linux2 -i /dev/video1 -vframes 1 test.jpeg]

---
Summary
- Having proper kernel support is sometimes a big assumption
- Unimplemented ioctls ?
- Unexpected behavior ?
- But we have a generic code which can run on multiple platforms !
- We have only discussed a very little part of the framework !

---
Sources
- https://fr.wikipedia.org/wiki/Video4Linux
- http://www.latelierducable.com/tv-televiseur/yuv-420-ycbcr-422-rgb-444-cest-quoi-le-chroma-subsampling/
- https://linuxtv.org/downloads/v4l-dvb-apis/uapi/v4l/v4l2.html
- http://linuxgizmos.com/libcamera-successor-to-v4l2-hopes-to-ease-embedded-linux-camera-headaches/